## Slide 1
Xiaoguang Guo
11/26/2023

## Slide 2: Outline
Problem definition
Data collection for real
Recording devices for real
Data preprocessing

## Slide 3: Problem Definition
Model M M(W) → C
Content of user conversations C with Alexa (the text of speeches)
WiFi traffic rate data W collected by Raspberry Pi
Questions:
  How to align C with W? By timestamps? Sync.
Notes: Can we collect simple dataset. Not long question.
And the beginning, From text to voice. https://pytorch.org/audio/stable/tutorials/tacotron2_pipeline_tutorial.html
TEXT-TO-SPEECH WITH TACOTRON2

## Slide 4: Data Collection for real
Configure Raspberry Pi as a WiFi router and data collector
Detect the WiFi traffic data(W) of Alexa Echo Dot through its IP
Design recording trigger mechanism
Record Alexa sessions by USB microphone when interactions happen
Save conversation audio files(A) and traffic data(W) with timestamps(T)
Transcribe the conversation recording for analysis using NLP(A -> C)
Align conversation content(C) with traffic data(W) based on timestamps(T).
Capture traffic rate data by Raspberry Pi (W)
Notes: Scapy, tcpdump,
Use pc to play audio
compared

## Slide 5: Recording Devices for real
USB microphone compatible with the Raspberry Pi 4 Model B.
  Blue Yeti
  Audio-Technica ATR2100x-USB
  Rode NT-USB
  Samson Go Mic
  Shure MV5
  Fifine Metal Condenser Recording Microphone
  …

## Slide 6: Data Preprocessing
Traffic Data
  Pattern recognition processing
  Time series analysis
  feature extraction
Notes: Accent & Background noise & Network latency

## Slide 8
Xiaoguang Guo
11/29/2023

## Slide 9: Outline
Data collection simple version
Datasets components
Traffic data components
Incoming/outgoing data
Sync text data with traffic data
Apply multiple different TTS models

## Slide 10: Data Collection Simple Version
Text Preparation: Create scripts of text(C)
Speech Synthesis: Use Tacotron2 to convert these texts into audio files (A)
Play Audio Files for Interaction: Play one speech at a time on Pi
Traffic data collection(W): Record the traffic data at the same time.

## Slide 11: Datasets Components
Ground True Data(C):
  User’s Input(C_u): The original text used to generate the speech.
  Alexa’s Response(C_r): The transcribed text from responses of Alexa.
Audio Data(A):
  User’s Input Audio(A_u):
    Generated from the user’s input text(C_u) by Tacotron2 in the simple version step.
    Recorded by Pi for real later.
  Alexa’s Response(A_r):
Traffic Data(W): Captured traffic data corresponding to interaction.

## Slide 12: Traffic Data Components:
Timestamps: When the interaction occurred
Source and Destination:
  Alexa Echo Dot’s IP: 10.3.141.158
  Amazon server’s IP: 3.217.147.217
Protocol: TCP, TLSv1.2
Packet Sizes: Sizes of the packets sent and received

## Slide 13: Incoming/Outgoing Data
Incoming data: 3.217.147.217 -> 10.3.141.158
  Amazon’s servers process the request and send back a response to Alexa. This response could include data for speech synthesis(Alexa’s reply), streaming audio, or control signals for smart home devices.
Outgoing data: 10.3.141.158 -> 3.217.147.217
  Alexa processes the audio and sends a request to Amazon’s servers. This request likely includes a digitized version of spoken command or query.

## Slide 14: Incoming/Outgoing Data
We must make sure that the traffic data have some patterns to learn.
Learn from incoming data?
  Both user’s input and the cloud response have contributions.
  We cannot get the response to the Alexa from cloud directly.
Learn from outgoing data?
  Only user’s audio input has contributions.
Questions:
  What is our motivation? Design a way to gain privacy?
  What is the application scenario? Attack and capture the traffic data so that the model can get what people said.
  Are Alexa’s responses important? I think attacker can get info from them. Maybe in the first step we can ignore the Alexa’s response.

## Slide 15: Sync Text Data with Traffic Data
Capture Duration:
  All captures should have the same duration time.
  Start from playing audio and sleep(12). And Stop.

## Slide 16: Apply Multiple Different TTS Models
One TTS model says 10 more times for one thing like “01234”, “Alexa”.
Maybe I can apply multiple models to generate ”0” audio files repeatedly.
Questions:
  Machine learning advice?

## Slide 18: Related Works
I Can Hear Your Alexa: Voice Command Fingerprinting on Smart Home Speakers. CNS’19
  ML models: LL-Jaccard, LL-NB, VNG++ and P-SVM
  Small real-word datasets(100 commands with 10 traffic traces per command)
  33.8% accuracy
Fingerprinting Encrypted Voice Traffic on Smart Speakers with Deep Learning. WiSec ’20
  DL models: CNN, LSTM, SAE
  Large not real-word datasets(1500 traffic traces per command)
  92.89% accuracy

## Slide 19: I Can Hear Your Alexa
33.8%
Real-word datasets

## Slide 20: Fingerprinting Encrypted Voice Traffic on Smart Speakers with Deep Learning.
Limitations:
  Synthetic dataset
  Use incoming traffic only
  Inferring the IP address of a smart speaker?

## Slide 22: Contribution
Design a voice attack system which can infer interaction contents via traffic data(inside attack or outside attack) without knowing ip.
Learning Method: Voice Traffic Data Fingerprinting

## Slide 23: PiVPN

## Slide 24: System Components
Router
Pi A (Wireless Access Point setup via RaspAP)
  Role: Acts as a Wireless Access Point
Pi B (VPN Server setup via PiVPN)
  Role: Serves as a VPN server(WireGurad)
Pi C (Alexa-Enabled device)
  Role: Functions as an Alexa-Enabled device for voice interactions
Maybe VPN Server can be integrated in Pi A(Wireless Access Point)

## Slide 25: Pi A Wireless Access Point
Role:

## Slide 26: Pi B VPN Server
Tasks:
  1. Generate VPN Configuration: ‘pivpn add’ to create a client profile for Pi C
  2. ufw: Uncomplicated Firewall
  3. Enable IP forwarding
  4. Configure NAT for the Wi-Fi Interface

## Slide 27: Pi C Alexa-Enable Device
Alexa Voice Service (AVS)
  AVS Device SDK Console Sample Application (Voice only)
  AVS Device SDK IPC Server Sample Application (Smart Screen device)
Alexa Skills Kit (ASK) CLI(Command Line Interface)
Set up the AVS Device SDK on Raspberry Pi
Notes: https://developer.amazon.com/en-US/docs/alexa/avs-device-sdk/smart-screen-raspberry-pi.html

## Slide 28: Review Last Disscussion
Question: Can we still attack if we don’t know actually ip or the ip is changing all the time.
VPN
  To answer the question: Can we still attack if people use VPN on a router?
  Also VPN will bring some noise traffic, more challenge
  But people typically don’t use VPN at their home I think. Not sure if it is a major contribution. Maybe a case study?
Turn Pi into an Alexa Echo
  Why? Make it easy for more operations: Keyboard interaction

## Slide 30: Questions
Can we do voice command fingerprint if knowing IP (Alexa & Amazon Server) and models of IoT Devices in smart home? Maybe Yes
In below scenario, can we still attack?
  The traffic data is encrypted by VPN.
  Don’t know the Amazon Server’s IP because of VPN.
  Don’t know the model of IoT devices in smart home.
  Don’t know the IP of IoT devices because the IP is changing all the time.
Is this scenario common?

## Slide 31
local eavesdropper
Why VPN?
Tunneling: can it hide Amazon Server’s IP?
Encryption: can it encrypt traffic?
Assumption Scenario:
Smart Speaker’s IP is changing all the time(DHCP? Leasing time?)
Amazon Server’s IP is hide because of VPN.
Traffic data is encrypted by VPN.
Don’t know the model of IoT devices.
Attacker Model:
Local eavesdropper(inside attack)?
What attacker can get?
If VPN Server is set in other place:
Outgoing: Alexa -> VPN?
Incoming: VPN -> Alexa
If VPN can only encrypt data:
Outgoing: Alexa -> Amazon Server
Incoming: Amazon Server -> Alexa

## Slide 32: Raspberry Pi Router
I want to set up OpenWrt on pi, and enable VPN on it.
Device:
  USB Wifi Adaptor
  Switch maybe
VPN: CyberGhost

## Slide 33: What finally model we want?
Input: whole-house traffic data.
Output: we can know which part of traffic is from Alexa or Google home, and the content of this traffic.
Maybe we can only focus on incoming data, because the response content of smart speaker is directly decided by incoming data and more fixed.