## Slide 1
Xiaoguang Guo
11/26/2023

## Slide 2: Outline
Problem definition
Data collection for real
Recording devices for real
Data preprocessing

## Slide 3: Problem Definition
Model M M(W) → C
Content of user conversations C with Alexa (the text of speeches)
WiFi traffic rate data W collected by Raspberry Pi
Questions:
  How to align C with W? By timestamps? Sync.
Notes: Can we collect simple dataset. Not long question.
And the beginning, From text to voice. https://pytorch.org/audio/stable/tutorials/tacotron2_pipeline_tutorial.html
TEXT-TO-SPEECH WITH TACOTRON2

## Slide 4: Data Collection for real
Configure Raspberry Pi as a WiFi router and data collector
Detect the WiFi traffic data(W) of Alexa Echo Dot through its IP
Design recording trigger mechanism
Record Alexa sessions by USB microphone when interactions happen
Save conversation audio files(A) and traffic data(W) with timestamps(T)
Transcribe the conversation recording for analysis using NLP(A -> C)
Align conversation content(C) with traffic data(W) based on timestamps(T).
Capture traffic rate data by Raspberry Pi (W)
Notes: Scapy, tcpdump,
Use pc to play audio
compared

## Slide 5: Recording Devices for real
USB microphone compatible with the Raspberry Pi 4 Model B.
  Blue Yeti
  Audio-Technica ATR2100x-USB
  Rode NT-USB
  Samson Go Mic
  Shure MV5
  Fifine Metal Condenser Recording Microphone
  …

## Slide 6: Data Preprocessing
Traffic Data
  Pattern recognition processing
  Time series analysis
  feature extraction
Notes: Accent & Background noise & Network latency

## Slide 8
Xiaoguang Guo
11/29/2023

## Slide 9: Outline
Data collection simple version
Datasets components
Traffic data components
Incoming/outgoing data
Sync text data with traffic data
Apply multiple different TTS models

## Slide 10: Data Collection Simple Version
Text Preparation: Create scripts of text(C)
Speech Synthesis: Use Tacotron2 to convert these texts into audio files (A)
Play Audio Files for Interaction: Play one speech at a time on Pi
Traffic data collection(W): Record the traffic data at the same time.

## Slide 11: Datasets Components
Ground True Data(C):
  User’s Input(C_u): The original text used to generate the speech.
  Alexa’s Response(C_r): The transcribed text from responses of Alexa.
Audio Data(A):
  User’s Input Audio(A_u):
    Generated from the user’s input text(C_u) by Tacotron2 in the simple version step.
    Recorded by Pi for real later.
  Alexa’s Response(A_r):
Traffic Data(W): Captured traffic data corresponding to interaction.

## Slide 12: Traffic Data Components:
Timestamps: When the interaction occurred
Source and Destination:
  Alexa Echo Dot’s IP: 10.3.141.158
  Amazon server’s IP: 3.217.147.217
Protocol: TCP, TLSv1.2
Packet Sizes: Sizes of the packets sent and received

## Slide 13: Incoming/Outgoing Data
Incoming data: 3.217.147.217 -> 10.3.141.158
  Amazon’s servers process the request and send back a response to Alexa. This response could include data for speech synthesis(Alexa’s reply), streaming audio, or control signals for smart home devices.
Outgoing data: 10.3.141.158 -> 3.217.147.217
  Alexa processes the audio and sends a request to Amazon’s servers. This request likely includes a digitized version of spoken command or query.

## Slide 14: Incoming/Outgoing Data
We must make sure that the traffic data have some patterns to learn.
Learn from incoming data?
  Both user’s input and the cloud response have contributions.
  We cannot get the response to the Alexa from cloud directly.
Learn from outgoing data?
  Only user’s audio input has contributions.
Questions:
  What is our motivation? Design a way to gain privacy?
  What is the application scenario? Attack and capture the traffic data so that the model can get what people said.
  Are Alexa’s responses important? I think attacker can get info from them. Maybe in the first step we can ignore the Alexa’s response.

## Slide 15: Sync Text Data with Traffic Data
Capture Duration:
  All captures should have the same duration time.
  Start from playing audio and sleep(12). And Stop.

## Slide 16: Apply Multiple Different TTS Models
One TTS model says 10 more times for one thing like “01234”, “Alexa”.
Maybe I can apply multiple models to generate ”0” audio files repeatedly.
Questions:
  Machine learning advice?